## Slide 1: Zybo “Audio Recorder”
Christopher Gutierrez
Cecs 561 // hardware/software codesign // spring 2019

## Slide 2: Introduction/Project Vision
Initial plan/functionality for the system
  Load music files (mp3, wav, etc) from microSD card to main memory
  Enable switches to each play a different sound
  Multiple switches enabled = sounds play on top of each other and create a “beat”
  Press push button 1 to record from Mic in
  Press push button 2 to playback (after all switches disabled)
  Press push button 0 to store in microSD card
Plan changed! More ahead…

## Slide 3: Challenges
Get the demo working
  Upgrade IPs
  Error running synthesis/generating bitstream
Issue where compiler wasn’t correctly locating BSP files
  Fixed by typing the entire file path where necessary
  Temporary Fix, need to look into where the files are located and move them around

## Slide 4: More challenges
Figuring out how the demo drivers work (more or less)
  Little to no documentation
  (A little) More on how it works later..
Every audio format (mp3, wav, aac) has different headers, sampling rates, etc.
  How to parse file such that the codec & accompanying drivers will interpret the data correctly? (Still don’t know)
  Some formats are fairly complicated (left channel samples, right channel samples, etc).. More research needed

## Slide 5: Current State
Same features as demo, with the following addition:
  Switches IP added to the design
  Each switch combination allows a different sound to be recorded & played back
  Total of 16 different 5 second tracks (woah)
  Tracks are automatically stored into the microSD card

## Slide 6: Hardware Design
IPs used (that we have already used in class)
  Push buttons (AXI GPIO)
  Dip switches (AXI GPIO)
  UART
  512 MB DDR3 Memory
New IPs
  Audio codec w/ 3.5 mm jacks
    Zybo board has a Line In jack, Mic In jack, and HPH Out jack
  Micro SD card connector

## Slide 7: Hardware Design – Block Diagram

## Slide 8: Hardware Design - d_axi_i2s_audio_0 IP Block
AXI_S2MM: Stream to Memory-mapped, transports data stream to DDR Memory
AXI_L: AXI interconnect signals
AXI_MM2S: Memory-mapped to stream, transports data from DDR memory to Audio Codec on PL

## Slide 9: Hardware Design – Enabling microSD
Enabled by default
Some tutorials included more complicated configurations, not necessary for my project
Must enable “xilffs” in BSP Settings in SDK (Xilinx Fat File System)

## Slide 10: Software Design
Function in “audio.c” used in the main loop to initiate the recording process (configures controller to receive data)
AxiDma: Driver API for the AXI DMA engine
u32NrSamples: Number of samples to record/playback
MEM_BASE_ADDR: DDR Base Address
fnAudioPlay function is very similar

## Slide 11: Software Design Modifications
Function in “audio.c” used in the main loop to initiate the playback process
While playing with different values for “MEM_BASE_ADDR”, realized I can dynamically allocate memory for “recordings” and pass the address to the record and play functions

## Slide 12: Software Mods Cont..
Add more memory to heap
  Previous Heap size was 1 KB, 40 MB is plenty
Each “track” is 1-2 MB, assuming they’re 2 MB, 2*16 = 32 MB, meaning plenty of memory

## Slide 13: SW Design Mods Cont..
Created a struct w/ a size of 2 MB so I could use the stdlib to dynamically allocate space for each recording

## Slide 14: More SW Stuff..
Allocating space in memory for the recordings (16 of them)
Mounting the SD card
Load recordings from file
“loadFromFile” function explained later..

## Slide 15: SW Modifications to “demo.c”
Snippets of code inside of main
Shows logic behind the what happens when you select a “track” and record over it
Shows logic behind the what happens when you select a “track” and play it back

## Slide 16: When recording is complete..

## Slide 17: Additional Functions
writeToFile – Takes a recording from memory and stuffs it into a file
loadFromFile – Takes a recording from a file and stuffs it into memory

## Slide 18: Future Work
If I somehow gain access to a board and Vivado again..
Figure out how to parse Wave files to work with demo codec/drivers
Add ability to play sounds on top of each other & record back to SD card

## Slide 19: References/Resources
Digilent Resources:
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/zybo-dma-audio-demo/start
  https://reference.digilentinc.com/learn/programmable-logic/tutorials/github-demos/start
Various Forums, Blogs, etc:
  https://forum.digilentinc.com/topic/4505-zybo-dma-audio-demo-error/#comment-17914
  https://forum.digilentinc.com/topic/4599-locked-ips-place_design-error-in-vivado-with-zybo-dma-audio-demo/
  https://forums.xilinx.com/t5/UltraScale-Architecture/XAxiDma-SimpleTransfer-and-Maximum-Transfer-Length/td-p/780556
  https://forums.xilinx.com/t5/Design-Entry/Vivado-2017-3-IP-Upgrade/td-p/813578
  https://forum.digilentinc.com/topic/9224-c-code-to-readwrite-to-ddr/
  https://forum.digilentinc.com/topic/1017-how-to-use-the-ddr-on-zybo/
  http://www.harald-rosenfeldt.de/2017/12/31/zynq-read-a-wav-file-from-sd-card-and-play-it-on-the-audio-codec/
  https://forums.xilinx.com/t5/Evaluation-Boards/Output-an-mp3-file-in-memory-card-to-audio-out-port-of-Zedboard/td-p/809606
  https://lauri.xn--vsandi-pxa.com/hdl/zynq/xilinx-dma.html
C-Programming Resources:
  https://www.cs.swarthmore.edu/~newhall/unixhelp/C_arrays.html#dynamic
  https://www.programiz.com/c-programming/c-dynamic-memory-allocation

## Slide 20: One more resource..
http://elm-chan.org/fsw/ff/00index_e.html?_ga=2.166515710.1152884192.1556995060-1875058106.1548301546

## Slide 21: Fin
Thanks.